## Slide 1: Arithmetic and Bitwise Operations on Binary Data CSCI 2400: Computer Architecture ECE 3217: Computer Architecture and Organization
Instructor:
David Ferry
Slides adapted from Bryant & O’Hallaron’s slides by Jason Fritts

## Slide 2: Arithmetic and Bitwise Operations
Operations
  Bitwise AND, OR, NOT, and XOR
  Logical AND, OR, NOT
  Shifts
  Complements
Arithmetic
  Unsigned addition
  Signed addition
  Unsigned/signed multiplication
  Unsigned/signed division

## Slide 3: Basic Processor Organization
Register file (active data)
  We’ll be a lot more specific later…
Arithmetic Logic Unit (ALU)
  Performs signed and unsigned arithmetic
  Performs logic operations
  Performs bitwise operations
Many other structures…
CPU
Register File
ALU
Memory

## Slide 4: Boolean Algebra
Developed by George Boole in 19th Century
  Algebraic representation of logic
    Encode “True” as 1 and “False” as 0
And
A&B = 1 when both A=1 and B=1
Or
A|B = 1 when either A=1 or B=1
Not
~A = 1 when A=0
Exclusive-Or (Xor)
A^B = 1 when either A=1 or B=1, but not both

## Slide 5: General Boolean Algebras
Operate on Bit Vectors
  Operations applied bitwise
  Bitwise-AND operator: &
  Bitwise-NOR operator: |
  Bitwise-XOR operator: ^
  Bitwise-NOT operator: ~
All of the Properties of Boolean Algebra Apply
01101001
& 01010101
01000001
01101001
| 01010101
01111101
01101001
^ 01010101
00111100
~ 01010101
10101010
01000001
01111101
00111100
10101010

## Slide 6: Quick Check
Operate on Bit Vectors
  Operations applied bitwise
  Bitwise-AND operator: &
  Bitwise-NOR operator: |
  Bitwise-XOR operator: ^
  Bitwise-NOT operator: ~
All of the Properties of Boolean Algebra Apply
01100110
& 00101111
01000001
11110000
| 01010101
0
01101001
^ 00001111
00111100
~ 00101111
10101010
00100110
11110101
01100110
11010000

## Slide 7: Bit-Level Operations in C
Operations &, |, ~, ^ Available in C
  Apply to any “integral” data type
    long, int, short, char, unsigned
  View arguments as bit vectors
  Arguments applied bit-wise
Examples (char data type):
  in hexadecimal in binary
  ~0x41 ➙ 0xBE // ~010000012 ➙ 101111102
  ~0x00 ➙ 0xFF // ~000000002 ➙ 111111112
  0x69 & 0x55 ➙ 0x41 // 011010012 & 010101012 ➙ 010000012
  0x69 | 0x55 ➙ 0x7D // 011010012 | 010101012 ➙ 011111012

## Slide 8: Contrast: Logic Operations in C
Contrast to Logical Operators
  &&, ||, !
    View 0 as “False”
    Anything nonzero as “True”
    Always return 0 or 1
    Early termination
Examples (char data type):
  !0x41 ➙ 0x00
  !0x00 ➙ 0x01
  !!0x41 ➙ 0x01
  0x69 && 0x55 ➙ 0x01
  0x69 || 0x55 ➙ 0x01
  p && *p // avoids null pointer access

## Slide 9: Bitwise Operations: Applications
Bit fields
  One byte can fit up to eight options in a single field
  Example: char flags = 0x1 | 0x4 | 0x8 = 000011012
  Test for a flag: if ( flags & 0x4 ){ //bit 3 is set } else { //bit 3 was not set }

## Slide 10: Shift Operations
Left Shift: x << y
  Shift bit-vector x left y places
      Throw away extra bits on left
    Fill with 0’s on right
Right Shift: x >> y
  Shift bit-vector x right y positions
    Throw away extra bits on right
  Logical shift
    Fill with 0’s on left
  Arithmetic shift
    Replicate most significant bit on right
Undefined Behavior
  Shift amount < 0 or ≥ word size
01100010
Argument x
00010000
<< 3
00011000
Log. >> 2
00011000
Arith. >> 2
10100010
Argument x
00010000
<< 3
00101000
Log. >> 2
11101000
Arith. >> 2
00010000
00010000
00011000
00011000
00011000
00011000
00010000
00101000
11101000
00010000
00101000
11101000

## Slide 11: Quick Check
Left Shift: x << y
  Shift bit-vector x left y places
      Throw away extra bits on left
    Fill with 0’s on right
Right Shift: x >> y
  Shift bit-vector x right y positions
    Throw away extra bits on right
  Logical shift
    Fill with 0’s on left
  Arithmetic shift
    Replicate most significant bit on right
Undefined Behavior
  Shift amount < 0 or ≥ word size
00110011
Argument x
00010000
<< 3
00011000
Log. >> 4
00011000
Arith. >> 3
1111111
Argument x
00010000
<< 3
00101000
Log. >> 4
11101000
Arith. >> 3
00010000
00011000
00011000
00010000
11101000

## Slide 12: Bitwise-NOT: One’s Complement
Bitwise-NOT operation: ~
  Bitwise-NOT of x is ~x
  Flip all bits of x to compute ~x
    flip each 1 to 0
    flip each 0 to 1
Complement
  Given x == 10011101
  Flip bits (one’s complement):
1
0
0
1
0
1
1
1
x:
0
1
1
0
1
0
0
0
~x:

## Slide 13: Signed Integer Negation: Two’s Complement
Negate a number by taking 2’s Complement
  Flip bits (one’s complement) and add 1
  ~x + 1 == -x
Negation (Two’s Complement):
  Given x == 10011101
  Flip bits (one’s complement):
  Add 1:
1
0
0
1
0
1
1
1
x:
0
1
1
0
1
0
0
0
~x:
+
1
0
1
1
0
1
1
0
0
-x:

## Slide 14: Complement & Increment Examples
x = 15213
x = 0

## Slide 15: Arithmetic and Bitwise Operations
Operations
  Bitwise AND, OR, NOT, and XOR
  Logical AND, OR, NOT
  Shifts
  Complements
Arithmetic
  Unsigned addition
  Signed addition
  Unsigned/signed multiplication
  Unsigned/signed division

## Slide 16: Unsigned Addition
Addition Operation
  Carry output dropped at end of addition
  Valid ONLY if true sum is within w-bit range
• • •
• • •
u
v
+
• • •
u + v
• • •
True Sum: w+1 bits
Operands: w bits
Discard Carry: w bits

## Slide 17: Unsigned Addition
Addition Operation
  Carry output dropped at end of addition
  Valid ONLY if true sum is within w-bit range
Example #1:
• • •
• • •
u
v
+
• • •
u + v
• • •
True Sum: w+1 bits
Operands: w bits
Discard Carry: w bits
0
1
1
0
1
0
0
0
9810
+
1
0
1
1
0
0
0
1
17210
0
1
0
0
1
0
0
1
7410
1
0
1
Valid in 8-bit
unsigned range

## Slide 18: Unsigned Addition
Example #2:
0
1
1
1
1
0
0
1
11010
+
0
0
1
0
0
0
1
1
5610
1
1
0
0
1
0
0
1
20210
1
1
1
Not Valid in 8-bit
unsigned range
(312 is > 255)
1
1
1

## Slide 19: Unsigned Addition
Example #2:
0
1
1
1
1
0
0
1
11010
+
0
0
1
0
0
0
1
1
5610
1
1
0
0
1
0
0
1
20210
1
1
1
Not Valid in 8-bit
unsigned range
(312 is > 255)
0
1
1
0
1
0
0
0
1008210
+
1
0
1
1
0
0
0
1
452410
0
1
0
0
1
0
0
1
5997810
1
1
1
1
1
1
Example #3:
0
0
1
1
1
1
0
0
1
1
1
0
1
0
0
1
0
0
0
0
0
1
1
0
1
1
1
1
1
1
Not Valid in 16-bit
unsigned range
(70060 is > 65535)

## Slide 20: Visualizing True Sum (Mathematical) Addition
Integer Addition
  4-bit integers u, v
  Compute true sum
  Values increase linearly with u and v
  Forms planar surface
u
v

## Slide 21: Visualizing Unsigned Addition
Wraps Around
  If true sum ≥ 2w
  At most once
0
2w
2w+1
u
v
True Sum
Modular Sum
Overflow
Overflow

## Slide 22: Two’s Complement Addition
Signed/Unsigned adds have Identical Bit-Level Behavior
  Signed vs. unsigned addition in C:
  int s, t, u, v;
  s = (int) ((unsigned) u + (unsigned) v);
  t = u + v
  Will give s == t
• • •
• • •
u
v
+
• • •
u + v
• • •
True Sum: w+1 bits
Operands: w bits
Discard Carry: w bits

## Slide 23: Signed Addition
Example #1:
0
1
1
1
1
0
0
1
11010
+
0
0
1
0
0
0
1
1
5610
1
1
0
0
1
0
0
1
-5410
1
1
1
Valid in 8-bit
signed range
(-128 < 56 < 127)
1
1
1
Example #2:
0
1
1
0
1
0
0
0
9810
+
1
0
1
1
0
0
0
1
-8410
0
1
0
0
1
0
0
1
7410
1
0
1
Note: Same bytes as for Ex #1 and Ex #2
in unsigned integer addition, but
now interpreted as 8-bit signed integers
Not Valid in 8-bit
signed range
(172 > 127)

## Slide 24: Visualizing Signed Addition
Values
  4-bit two’s comp.
  Range from -8 to +7
Wraps Around
  If sum  2w–1
    Becomes negative
    At most once
  If sum < –2w–1
    Becomes positive
    At most once
u
v
Positive Overflow
Negative Overflow

## Slide 25: Multiplication
Goal: Computing Product of w-bit numbers x, y
  Either signed or unsigned
But, exact results can be bigger than w bits
  Unsigned: up to 2w bits
    Result range: 0 ≤ x * y ≤ (2w – 1) 2 = 22w – 2w+1 + 1
  Two’s complement min (negative): Up to 2w-1 bits
    Result range: x * y ≥ (–2w–1)*(2w–1–1) = –22w–2 + 2w–1
  Two’s complement max (positive): Up to 2w bits, but only for (SMinw)2
    Result range: x * y ≤ (–2w–1) 2 = 22w–2
So, maintaining exact results…
  would need to keep expanding word size with each product computed
  is done in software, if needed
    e.g., by “arbitrary precision” arithmetic packages

## Slide 26: Unsigned Multiplication in C
Standard Multiplication Function
  Ignores high order w bits
Implements Modular Arithmetic
  machine(u · v) = true(u · v) mod 2w
• • •
• • •
u
v
*
• • •
u · v
• • •
True Product: 2*w bits
Operands: w bits
Discard w bits: w bits
• • •

## Slide 27: Signed Multiplication in C
Standard Multiplication Function
  Ignores high order w bits
  Some of which are different for signed vs. unsigned multiplication
  Lower bits are the same
• • •
• • •
u
v
*
• • •
u · v
• • •
True Product: 2*w bits
Operands: w bits
Discard w bits: w bits
• • •

## Slide 28: True Binary Multiplication
Multiply positive integers using the same place-value algorithm you learned in grade school
12310
23410
492
X
3690
+ 24600
2878210

## Slide 29: True Binary Multiplication
Multiply positive integers using the same place-value algorithm you learned in grade school
12310
23410
492
X
3690
+ 24600
2878210
0
1
1
0
1
1
1
1
12310
1
1
1
0
1
0
0
1
23410
X

## Slide 30: True Binary Multiplication
Multiply positive integers using the same place-value algorithm you learned in grade school
12310
23410
492
X
3690
+ 24600
2878210
0
1
1
0
1
1
1
1
12310
1
1
1
0
1
0
0
1
23410
X
0
0
0
0
0
0
0
0

## Slide 31: True Binary Multiplication
Multiply positive integers using the same place-value algorithm you learned in grade school
12310
23410
492
X
3690
+ 24600
2878210
0
1
1
0
1
1
1
1
12310
1
1
1
0
1
0
0
1
23410
X
0
0
0
0
0
0
0
0
0
1
1
0
1
1
1
1

## Slide 32: True Binary Multiplication
Multiply positive integers using the same place-value algorithm you learned in grade school
12310
23410
492
X
3690
+ 24600
2878210
0
1
1
0
1
1
1
1
12310
1
1
1
0
1
0
0
1
23410
X
0
0
0
0
0
0
0
0
0
1
1
0
1
1
1
1
0
0
0
0
0
0
0
0

## Slide 33: True Binary Multiplication
Multiply positive integers using the same place-value algorithm you learned in grade school
12310
23410
492
X
3690
+ 24600
2878210
0
1
1
0
1
1
1
1
12310
1
1
1
0
1
0
0
1
23410
X
0
0
0
0
0
0
0
0
0
1
1
0
1
1
1
1
0
1
1
0
1
1
1
1
0
0
0
0
0
0
0
0

## Slide 34: True Binary Multiplication
Multiply positive integers using the same place-value algorithm you learned in grade school
12310
23410
492
X
3690
+ 24600
2878210
0
1
1
0
1
1
1
1
12310
1
1
1
0
1
0
0
1
23410
X
0
0
0
0
0
0
0
0
0
1
1
0
1
1
1
1
0
1
1
0
1
1
1
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
1
0
1
1
1
1
0
1
1
0
1
1
1
1
0
1
1
0
1
1
1
1
+
0
1
1
1
1
0
0
1
2878210
0
1
1
0
0
0
1
0

## Slide 35: Power-of-2 Multiply with Shift
Consider:
610 * 210 = 1210
1
1
0
0
610
0
1
0
0
210
X

## Slide 36: Power-of-2 Multiply with Shift
Consider:
610 * 210 = 1210
1
1
0
0
610
0
1
0
0
210
X
0
0
0
0
0
0
0
0
1
1
0
0
0
0
0
0
+
1
0
0
1
1210

## Slide 37: Power-of-2 Multiply with Shift
Consider:
Multiplying by two always shifts the input bit pattern by one to the left. That is:
More generally- multiplying by 2k always shifts the input by k to the left:
610 * 210 = 1210
1
1
0
0
610
0
1
0
0
210
X
0
0
0
0
0
0
0
0
1
1
0
0
0
0
0
0
+
1
0
0
1
1210
(610 * 210 ) == (01102 << 1)
(x10 * 2k ) == (x2 << k)

## Slide 38: Power-of-2 Multiply with Shift
Operation
  u << k gives u * 2k
  Both signed and unsigned
Examples
  u << 3 == u * 8
  (u << 5) – (u << 3) == u * 24
  Most machines shift and add faster than multiply
    Compiler generates this code automatically
• • •
0
0
1
0
0
0
•••
u
2k
*
u · 2k
True Product: w+k bits
Operands: w bits
Discard k bits: w bits
•••
k
• • •
0
0
0
•••
0
0
0
•••
•••

## Slide 39: Unsigned Power-of-2 Divide with Shift
Quotient of Unsigned by Power of 2
  u >> k gives  u / 2k 
  Uses logical shift
0
0
1
0
0
0
•••
u
2k
/
u / 2k
Division:
Operands:
•••
k
•••
•••
•••
0
0
0
•••
•••
 u / 2k 
•••
Result:
.
Binary Point
0
0
0
0
•••
0

## Slide 40: Signed Power-of-2 Divide with Shift
Quotient of Signed by Power of 2
  x >> k gives  x / 2k 
  Uses arithmetic shift
  Rounds wrong direction when u < 0
0
0
1
0
0
0
•••
x
2k
/
x / 2k
Division:
Operands:
•••
k
•••
•••
•••
0
•••
•••
RoundDown(x / 2k)
•••
Result:
.
Binary Point
0
•••

## Slide 41: Incorrect Power-of-2 Divide
Consider: -25 / 2
We expect that -25 / 2 = -12, however:
-2510 = 111001112
(-25 / 2 ) becomes (111001112 >> 1)
(111001112 >> 1) = 111100112
111100112 = -13

## Slide 42: Correct Power-of-2 Divide with Biasing
Quotient of Negative Number by Power of 2
  Want  x / 2k  (Round Toward 0)
  Compute as  (x+2k-1)/ 2k 
    In C: (x + (1<<k)-1) >> k
    Biases dividend toward 0
Case 1: No rounding
Divisor:
Dividend:
0
0
1
0
0
0
•••
u
2k
/
 u / 2k 
•••
k
1
•••
0
0
0
•••
1
•••
0
1
1
•••
.
Binary Point
1
0
0
0
1
1
1
•••
+2k –1
•••
1
1
1
•••
1
•••
1
1
1
•••
    Biasing has no effect
Dividend’s low bits are zero

## Slide 43: Biasing without changing result
Consider: -20 / 4 (answer should be -5)
Without bias:
-2010 = 111011002
(-20 / 4 ) becomes (111011002 >> 2)
(111011002 >> 2) = 111110112
111110112 = -5
With bias:
-2010 + 310 = 111011112
(-23 / 4 ) becomes (111011112 >> 2)
(111011112 >> 2) = 111110112
111110112 = -5

## Slide 44: Correct Power-of-2 Divide (Cont.)
Divisor:
Dividend:
Case 2: Rounding
0
0
1
0
0
0
•••
x
2k
/
 x / 2k 
•••
k
1
•••
•••
1
•••
0
1
1
•••
.
Binary Point
1
0
0
0
1
1
1
•••
+2k –1
•••
1
•••
•••
    Biasing adds 1 to final result
•••
Incremented by 1
Incremented by 1
Nonzero low bits

## Slide 45: Biasing that does change the result
Consider: -21 / 4 (answer should be -5)
Without bias:
-2110 = 111010112
(-21 / 4 ) becomes (111010112 >> 2)
(111010112 >> 2) = 111110102
111110102 = -6 (incorrect!)
With bias:
-2110 + 310 = 111011102
(-18 / 4 ) becomes (111011102 >> 2)
(111011102 >> 2) = 111110112
111110112 = -5

## Slide 46: Biasing that does change the result
Consider: -21 / 4 (answer should be -5)
Without bias:
-2110 = 111010112
(-21 / 4 ) becomes (111010112 >> 2)
(111010112 >> 2) = 111110102
111110102 = -6 (incorrect!)
With bias:
-2110 + 310 = 111011102
(-18 / 4 ) becomes (111011102 >> 2)
(111011102 >> 2) = 111110112
111110112 = -5
Recall- lowest
order bit has
value 1!

## Slide 47: Arithmetic: Basic Rules
Unsigned ints, 2’s complement ints are isomorphic rings: isomorphism = casting
Left shift
  Unsigned/signed: multiplication by 2k
  Always logical shift
Right shift
  Unsigned: logical shift, div (division + round to zero) by 2k
  Signed: arithmetic shift
    Positive numbers: div (division + round to zero) by 2k
    Negative numbers: div (division + round away from zero) by 2k Use biasing to fix