## Slide 1: Data Representation – Floating Point CSCI 2400 / ECE 3217: Computer Architecture
Instructor:
David Ferry
Slides adapted from Bryant & O’Hallaron’s slides
via Jason Fritts

## Slide 2: Today: Floating Point
Background: Fractional binary numbers
Example and properties
IEEE floating point standard: Definition
Floating point in C
Summary

## Slide 3: Fractional binary numbers
What is 1011.1012?
How can we express fractions like ¼ in binary?

## Slide 4: Place-Value Fractional Binary Numbers
2i
2i-1
22 = 4
21 = 2
20 = 1
2-1 = 1/2
2-2 = 1/4
2-3 = 1/8
2-j
bi | bi-1 | ••• | b2 | b1 | b0 | b-1 | b-2 | b-3 | ••• | b-j
• • •
Representation
  Bits to right of “binary point” represent fractional powers of 2
  Represents rational number:
• • •
Notes: Latex source for equation: \sum_{k=-j}^i b_k \times 2^k

## Slide 5: Fractional Binary Numbers: Examples
Value Representation
  101.112
  010.1112
  000.0110012
Observations
  Divide by 2 by shifting right
  Multiply by 2 by shifting left
Limitations
  Can only exactly represent numbers of the form x/2k
  Other rational numbers have repeating bit representations
  Value Representation
1/3 0.0101010101[01]…2
1/5 0.001100110011[0011]…2
Limited range when used with “fixed point” representations

## Slide 6: Quick Check
Convert:
255 9⁄16 to binary
10101.101012 to decimal

## Slide 7: Quick Check
Suppose an 8-bit fixed-point representation with:
One sign bit
Four integer bits
Three fractional bits
Convert:
  110101102 to decimal
What bit pattern(s) have the largest positive value? What is it?
What bit pattern(s) have the value closest to zero?
What bit pattern(s) have the value of zero?
s | integer | fractional
1 | 4-bits | 3-bits

## Slide 8: Today: Floating Point
Background: Fractional binary numbers
Example and properties
IEEE floating point standard: Definition
Floating point in C
Summary

## Slide 9: Floating Point Representation
Similar to scientific notation
E.g.:
E.g.:
FP is this concept but with an efficient binary format! But…
  Uses base 2 instead of base 10
  Places restrictions on how certain values are represented
  Deals with finiteness of representation

## Slide 10: Floating Point Representation
Numerical Form: (–1)s M 2E
  Sign bit s determines whether number is negative or positive
  Significand (mantissa) M normally a fractional value in range [1.0, 2.0)
  Exponent E weights value by power of two
Encoding
  s is sign bit s
  exp field encodes E (but is not equal to E)
  frac field encodes M (but is not equal to M)
s | exp | frac

## Slide 11: Tiny Floating Point Example
8-bit Floating Point Representation
  the sign bit is in the most significant bit
  the next four bits are the exponent (exp), with a bias of 24-1 - 1 = 7
  the last three bits are the fraction (frac)
Exponent bias
  enable exponent to represent both positive and negative powers of 2
  use half of range for positive and half for negative power
  given k exponent bits, bias is then 2k-1 - 1
s | exp | frac
1 | 4-bits | 3-bits

## Slide 12: Floating Point Encodings and Visualization
+
−
0
+Denorm
+Normalized
−Denorm
−Normalized
+0
NaN
NaN
Five encodings:
  Two general forms: normalized, denormalized
  Three special values: zero, infinity, NaN (not a number)
  Name Exponent(exp) Fraction(frac)
    zero exp == 0000 frac == 000
    denormalized exp == 0000 frac != 000
    normalized 0000 < exp < 1111 frac != 000
    infinity exp == 1111 frac == 000
    NaN exp == 1111 frac != 000

## Slide 13: Dynamic Range (Positives)
s exp frac E Value
0 0000 000 -6 0
0 0000 001 -6 1/8*1/64 = 1/512
0 0000 010 -6 2/8*1/64 = 2/512
…
0 0000 110 -6 6/8*1/64 = 6/512
0 0000 111 -6 7/8*1/64 = 7/512
0 0001 000 -6 8/8*1/64 = 8/512
0 0001 001 -6 9/8*1/64 = 9/512
…
0 0110 110 -1 14/8*1/2 = 14/16
0 0110 111 -1 15/8*1/2 = 15/16
0 0111 000 0 8/8*1 = 1
0 0111 001 0 9/8*1 = 9/8
0 0111 010 0 10/8*1 = 10/8
…
0 1110 110 7 14/8*128 = 224
0 1110 111 7 15/8*128 = 240
0 1111 000 n/a inf
0 1111 xxx n/a NaN
closest to zero
largest denorm
smallest norm
closest to 1 below
closest to 1 above
largest norm
Denormalized
numbers
Normalized
numbers
infinity
NaN (not a number)
v = (–1)s M 2E
norm: E = Exp – Bias
denorm: E = 1 – Bias

## Slide 14: Distribution of Values
6-bit IEEE-like format
  e = 3 exponent bits
  f = 2 fraction bits
  Bias is 23-1-1 = 3
Notice how the distribution gets denser toward zero.
s | exp | frac
1 | 3-bits | 2-bits
8 denormalized values
(blowup of -1 → 1)
(reduced format from 8 bits
to 6 bits for visualization)

## Slide 15: Quick Check
10-bit IEEE-like format
  e = 5 exponent bits
  f = 4 fraction bits
What is the exponent bias?
s | exp | frac
1 | 5-bits | 4-bits

## Slide 16: Quick Check
10-bit IEEE-like format
  e = 5 exponent bits
  f = 4 fraction bits
What is the exponent bias?
s | exp | frac
1 | 5-bits | 4-bits

## Slide 17: Quick Check
10-bit IEEE-like format
  e = 5 exponent bits
  f = 4 fraction bits
What is the exponent bias?
How many denormalized numbers are there?
s | exp | frac
1 | 5-bits | 4-bits

## Slide 18: Quick Check
10-bit IEEE-like format
  e = 5 exponent bits
  f = 4 fraction bits
What is the exponent bias?
How many denormalized numbers are there?
  Exponent = , so 24 positive and 24 negative
s | exp | frac
1 | 5-bits | 4-bits

## Slide 19: Quick Check
10-bit IEEE-like format
  e = 5 exponent bits
  f = 4 fraction bits
What is the exponent bias?
How many denormalized numbers are there?
  Exponent = , so 24 positive and 24 negative
What is the bit pattern of the maximum value number?
What is the bit pattern of the number closest to zero?
s | exp | frac
1 | 5-bits | 4-bits

## Slide 20: Quick Check
10-bit IEEE-like format
  e = 5 exponent bits
  f = 4 fraction bits
What is the exponent bias?
How many denormalized numbers are there?
  Exponent = , so 24 positive and 24 negative
What is the bit pattern of the maximum value number?
  Sign = 0, Exponent = 11110, frac=1111, so 0111101111
What is the bit pattern of the number closest to zero?
  Sign = ?, Exponent = 00000, frac=0001, so ?000000001
s | exp | frac
1 | 5-bits | 4-bits

## Slide 21: Quick Check
10-bit IEEE-like format
  e = 5 exponent bits
  f = 4 fraction bits
What is the bit pattern of the smallest positive normal number?
s | exp | frac
1 | 5-bits | 4-bits

## Slide 22: Quick Check
10-bit IEEE-like format
  e = 5 exponent bits
  f = 4 fraction bits
What is the bit pattern of the smallest positive normal number?
  Sign = 0, exp = 00001, frac = 0000; so 0000010000
s | exp | frac
1 | 5-bits | 4-bits

## Slide 23: Quick Check
10-bit IEEE-like format
  e = 5 exponent bits
  f = 4 fraction bits
What is the bit pattern of the smallest positive normal number?
  Sign = 0, exp = 00001, frac = 0000; so 0000010000
What is the value of the smallest positive normal number?
s | exp | frac
1 | 5-bits | 4-bits

## Slide 24: Quick Check
10-bit IEEE-like format
  e = 5 exponent bits
  f = 4 fraction bits
What is the bit pattern of the smallest positive normal number?
  Sign = 0, exp = 00001, frac = 0000; so 0000010000
What is the value of the smallest positive normal number?
  Value =
  S = 0
  Exponent bias = 15, so E = 1 - 15 = -14
  M = = 1
  Value = = = 0.00006103515
s | exp | frac
1 | 5-bits | 4-bits

## Slide 25: Quick Check
10-bit IEEE-like format
  e = 5 exponent bits
  f = 4 fraction bits
Given a 32-bit floating point number, and a 32-bit integer, which can represent more discrete values?
s | exp | frac
1 | 5-bits | 4-bits

## Slide 26: Quick Check
10-bit IEEE-like format
  e = 5 exponent bits
  f = 4 fraction bits
Given a 32-bit floating point number, and a 32-bit integer, which can represent more discrete values?
  Both can represent 232 values, but some bit patterns duplicate values, e.g. +0/-0, +/-, and many NaNs (exponent = 11…1, frac != 00…0)
s | exp | frac
1 | 5-bits | 4-bits

## Slide 27: Today: Floating Point
Background: Fractional binary numbers
Example and properties
IEEE floating point standard: Definition
Floating point in C
Summary

## Slide 28: IEEE Floating Point
IEEE Standard 754
  Established in 1985 as uniform standard for floating point arithmetic
    Before that, many idiosyncratic formats
  Supported by all major CPUs
Driven by numerical concerns
  Nice standards for rounding, overflow, underflow
  Hard to make fast in hardware
    Numerical analysts predominated over hardware designers in defining standard

## Slide 29: Floating Point Representation
Numerical Form: (–1)s M 2E
  Sign bit s determines whether number is negative or positive
  Significand (mantissa) M normally a fractional value in range [1.0, 2.0)
  Exponent E weights value by power of two
Encoding
  s is sign bit s
  exp field encodes E (but is not equal to E)
  frac field encodes M (but is not equal to M)
s | exp | frac

## Slide 30: Precisions
Single precision: 32 bits (c type: float)
Double precision: 64 bits (c type: double)
Extended precision: 80 bits (Intel only)
s | exp | frac
1 | 8-bits | 23-bits
s | exp | frac
1 | 11-bits | 52-bits
s | exp | frac
1 | 15-bits | 63 or 64-bits

## Slide 31: Normalized Values
Condition: exp ≠ 000…0 and exp ≠ 111…1
Exponent coded as biased value: E = Exp – Bias
  Exp: unsigned value of exp field
  Bias = 2k-1 - 1, where k is number of exponent bits
    Single precision: 127 (exp: 1…254  E: -126…127)
    Double precision: 1023 (exp: 1…2046  E: -1022…1023)
Significand coded with implied leading 1: M = 1.xxx…x2
  xxx…x: bits of frac
Decimal value of normalized FP representations:
  Single-precision:
  Double-precision:

## Slide 32: Normalized Encoding Example
Value: float F = 15213.0;
  1521310 = 111011011011012
  = 1.11011011011012 x 213
Significand
  M = 1.11011011011012
  frac = 110110110110100000000002
Exponent (E = Exp – Bias)
  E = 13
  Bias = 127
  Exp = E + Bias = 140 = 100011002
0 10001100 11011011011010000000000
s
exp
frac
shift binary point by K bits so that
only one leading 1 bit remains on
the left side of the binary point
(here, shifted right by 13 bits, so K = 13),
then multiply by 2K (here, 213)

## Slide 33: Denormalized Values
Condition: exp = 000…0
Exponent value: E = –Bias + 1 (instead of E = 0 – Bias)
Significand coded with implied leading 0: M = 0.xxx…x2
  xxx…x: bits of frac
Cases
  exp = 000…0, frac = 000…0
    Represents zero value
    Note distinct values: +0 and –0 (why?)
  exp = 000…0, frac ≠ 000…0
    Numbers very close to 0.0
    Lose precision as get smaller
    Equispaced

## Slide 34: Special Values
Special condition: exp = 111…1
Case: exp = 111…1, frac = 000…0
  Represents value  (infinity)
  Operation that overflows
  Both positive and negative
  E.g., 1.0/0.0 = −1.0/−0.0 = +, 1.0/−0.0 = −
Case: exp = 111…1, frac ≠ 000…0
  Not-a-Number (NaN)
  Represents case when no numeric value can be determined
  E.g., sqrt(–1),  − ,   0

## Slide 35: Interesting Numbers
Description exp frac Numeric Value
Zero 00…00 00…00 0.0
Smallest Pos. Denorm. 00…00 00…01 2– {23,52} x 2– {126,1022}
  Single ≈ 1.4 x 10–45
  Double ≈ 4.9 x 10–324
Largest Denormalized 00…00 11…11 (1.0 – ε) x 2– {126,1022}
  Single ≈ 1.18 x 10–38
  Double ≈ 2.2 x 10–308
Smallest Pos. Normalized 00…01 00…00 1.0 x 2– {126,1022}
  Just larger than largest denormalized
One 01…11 00…00 1.0
Largest Normalized 11…10 11…11 (2.0 – ε) x 2{127,1023}
  Single ≈ 3.4 x 1038
  Double ≈ 1.8 x 10308
{single,double}

## Slide 36: Today: Floating Point
Background: Fractional binary numbers
Example and properties
IEEE floating point standard: Definition
Floating point in C
Summary

## Slide 37: Floating Point in C
C Guarantees Two Levels
  float single precision
  double double precision
Conversions/Casting
  Casting between int, float, and double changes bit representation
  double/float → int
    Truncates fractional part
    Like rounding toward zero
    Not defined when out of range or NaN: Generally sets to TMin
  int → double
    Exact conversion, as long as int has ≤ 53 bit word size
  int → float
    Will round according to rounding mode

## Slide 38: Today: Floating Point
Background: Fractional binary numbers
Example and properties
IEEE floating point standard
Rounding, addition, multiplication
Floating point in C
Summary

## Slide 39: Floating Point Operations: Basic Idea
x +f y = Round(x + y)
x f y = Round(x  y)
Basic idea
  First compute exact result
  Make it fit into desired precision
    Possibly overflow if exponent too large
    Possibly round to fit into frac

## Slide 40: Rounding
Rounding Modes (illustrate with $ rounding)
$1.40 $1.60 $1.50 $2.50 –$1.50
  Towards zero $1 $1 $1 $2 –$1
  Round down (−) $1 $1 $1 $2 –$2
  Round up (+) $2 $2 $2 $3 –$1
  Nearest Even (default) $1 $2 $2 $2 –$2

## Slide 41: Closer Look at Round-To-Even
Default Rounding Mode
  Hard to get any other kind without dropping into assembly
  All others are statistically biased
    Sum of set of positive numbers will consistently be over- or under- estimated
Applying to Other Decimal Places / Bit Positions
  When exactly halfway between two possible values
    Round so that least significant digit is even
  E.g., round to nearest hundredth
    7.8949999 7.89 (Less than half way)
    7.8950001 7.90 (Greater than half way)
    7.8950000 7.90 (Half way—round up)
    7.8850000 7.88 (Half way—round down)

## Slide 42: Rounding Binary Numbers
Binary Fractional Numbers
  “Even” when least significant bit is 0
  “Half way” when bits to right of rounding position = 100…2
Examples
  Round to nearest 1/4 (2 bits right of binary point)
  Value Binary Rounded Action Rounded Value
  2 3/32 10.000112 10.002 (<1/2—down) 2
  2 3/16 10.001102 10.012 (>1/2—up) 2 1/4
  2 7/8 10.111002 11.002 ( 1/2—up) 3
  2 5/8 10.101002 10.102 ( 1/2—down) 2 1/2

## Slide 43: Scientific Notation Multiplication
= ?
Compute result by pieces:
  Sign : signleft * signright = 1*1 = 1
  Significand : Mleft * Mright = 2.5 * 3.0 = 7.5
  Exponent : Eleft + Eright = 3 + 2 = 5
  Result:

## Slide 44: FP Multiplication
(–1)s1 M1 2E1 x (–1)s2 M2 2E2
Exact Result: (–1)s M 2E
  Sign s: s1 ^ s2
  Significand M: M1 x M2
  Exponent E: E1 + E2
Fixing
  If M ≥ 2, shift M right, increment E
  If E out of range, overflow
  Round M to fit frac precision
Implementation
  Biggest chore is multiplying significands

## Slide 45: Scientific Notation Addition
= ?
Assume Eleft is larger that Eright
Align by decimal point:
  Significand : 2.5 + .3 2.8
  Exponent : E = Eleft = 3
  Result:

## Slide 46: Floating Point Addition
(–1)s1 M1 2E1 + (-1)s2 M2 2E2
  Assume E1 > E2
Exact Result: (–1)s M 2E
  Sign s, significand M:
    Result of signed align & add
  Exponent E: E1
Fixing
  If M ≥ 2, shift M right, increment E
  if M < 1, shift M left k positions, decrement E by k
  Overflow if E out of range
  Round M to fit frac precision
(–1)s1 M1
(–1)s2 M2
E1–E2
+
(–1)s M
Get binary points lined up

## Slide 47: Mathematical Properties of FP Add
Compare to those of Abelian Group
  Commutative?
  (a + b) = (b + a)
  Associative?
    Overflow and inexactness of rounding
    (3.14+1e10)-1e10 = 0, 3.14+(1e10-1e10) = 3.14
Yes
No

## Slide 48: Mathematical Properties of FP Mult
Compare to Commutative Ring
  Multiplication Commutative?
  Ex: (1e20*1e-20)=(1e-20*1e20)
  Multiplication is Associative?
    Possibility of overflow, inexactness of rounding
    Ex: (1e20*1e20)*1e-20= inf, 1e20*(1e20*1e-20)= 1e20
  Multiplication distributes over addition?
    Possibility of overflow, inexactness of rounding
    1e20*(1e20-1e20)= 0.0, 1e20*1e20 – 1e20*1e20 = NaN
Yes
No
No

## Slide 49: Summary
Represents numbers of form M x 2E
One can reason about operations independent of implementation
  As if computed with perfect precision and then rounded
Not the same as real arithmetic
  Violates associativity/distributivity
  Makes life difficult for compilers & serious numerical applications programmers